## Slide 1
GITAM (Deemed-to-be) University
www.gitam.edu
Department of Electrical Electronics and Communication Engineering
Project Team:
Bharath Narasimha Sai-BU22EECE0100184
Gannoju Om Prakash Chary-BU22EECE0100304
Abhishek Hiremath-BU22EECE0100448
Project Mentor:
Dr. Kamalanathan C
Project In-charge:
Dr. Subhashish Tiwari
QoS-Aware Seamless Vertical Handoff in Heterogeneous Wireless Networks using SDN and MIPv6
Review-II
AY 2025-26
Capstone Project – Introduction (PROJ2999)

## Slide 2
Objective and Goals
Objective
Goals
Design a centralized SDN controller for real-time vertical handoff management between heterogeneous wireless networks (Wi-Fi, LTE, 5G).
Develop a hybrid Fuzzy-TOPSIS multi-criteria decision algorithm using QoS parameters: RSSI, bandwidth, latency, packet loss, and cost.
Integrate Mobile IPv6 (MIPv6) for seamless IP address continuity and session persistence during handovers.
Implement and validate the framework through Python-based simulation measuring handover latency, packet loss, and ping-pong events.
Compare performance against existing approaches and investigate scalability for future 5G/6G networks.
Design and implement an intelligent handoff system for heterogeneous wireless networks that ensures seamless connectivity and maintains high Quality of Service (QoS), leveraging Software Defined Networking (SDN) and Mobile IPv6 (MIPv6) for dynamic and efficient mobility management.

## Slide 3
Project Plan

## Slide 4
Title and Author | Problem Statement | Methodology | Result
Dynamic Mobility and Handover Management in SDN-Based 5G HetNets Khan et al., 2024 | Frequent and unnecessary handovers in dense heterogeneous networks degrade QoS and increase signaling overhead. | Multi-parameter best cell selection using SDN controller. Algorithm based on RSS, load, dwell time, direction. Simulated in 5G HetNet scenario. | 39% reduction in handovers; improved throughput and lower delay. SDN enables efficient, dynamic mobility.
QoS-Aware and Fault-Tolerant Handovers in SDN-Based 5G Networks Recent Supporting Paper | Vertical handoffs can cause packet loss, latency spikes, and service disruption, especially in real-time apps. | SDN-based centralized control with QoS criteria. Fault-tolerant handover logic tested in wireless emulation environments. | Enhanced QoS during handoff. Fault-tolerance reduces service interruption. Improved performance for multimedia apps.
Literature Survey

## Slide 5
Machine Learning for Handover Decision in 6G Networks Recent Publication (2025) | Classical handover methods fail to predict user movement and network load, impacting handoff quality. | ML algorithms trained with user mobility and network data. Edge computing assists handover prediction and selection. | Higher handoff accuracy and lower delay. Dynamic adjustment to network conditions, useful for future 6G scenarios.
SDN-Based Distributed Mobility Management for 5G Networks Eurecom White Paper | Traditional mobility management lacks scalability and quick adaptability for multiple user types and diverse apps. | SDN and DMM integration, centralized flow management, simulation in cloud-based testbed. | Reduced signaling load, rapid handoff response, scalable to large networks. Successful dynamic handoff management.

## Slide 6
QOS Aware Vertical Handover Process in Heterogeneous Wireless Networks Santhi and Prabha, 2023 | Vertical handoffs must meet QoS constraints such as delay, jitter, bandwidth, security, and cost. | Combined multiple analytic network process (M-ANP) and TOPSIS for network selection satisfying QoS constraints. | Enhanced QoS-aware network selection for vertical handoffs, validated through simulation.
Enhancing QoS Through SDN in Wireless Networks Ait Oulahyane, 2023 | Addressing unreliable access points and dynamic access control to maintain QoS in wireless networks. | Proposed SDN-based secure model for dynamic access control and QoS management. Tested using SDN controllers and real scenarios. | Improved connection reliability and QoS enforcement in wireless networks through SDN-enabled control.

## Slide 7
Architecture
Structural Diagram:
Block Diagram/Pin Diagram
Behaviour Diagram
Flow chart/ State machine

## Slide 8
Use Cases & Testing
Test Cases:
Handover Latency Measurement: Verify vertical handoff delay (Wi-Fi to LTE/5G) is within acceptable limits (<50 ms)
Packet Loss Assessment: Measure packet loss during handoff at different user speeds; target <1% loss
Throughput Stability: Test throughput before, during, and after handoff for consistent QoS
Handover Trigger Accuracy: Verify handoff initiates based on multi-criteria thresholds (RSSI, load, latency)
Ping-Pong Avoidance: Confirm no rapid back-and-forth handovers between same networks
MIPv6 Address Continuity: Validate IP address persistence across network changes
Load Balancing Effectiveness: Ensure handoff distributes users across cells efficiently
High-Speed Mobility: Test reliability at vehicular speeds (>60 km/h)
Use Cases
Urban Commuter: User transitions from home Wi-Fi → Metro LTE → Office Wi-Fi with ongoing video call
Highway Driver: Vehicular handoff across multiple LTE cells maintaining navigation and music streaming
Dense Stadium Event: Mass handoff coordination for 50,000+ users during sports event
Enterprise Campus: Seamless indoor/outdoor Wi-Fi/5G transitions for remote desktop session
Emergency Services: Priority handoff for first responders maintaining mission-critical communications

## Slide 9
Implementation and Results – Iteration 1
Iteration 1: Core Module Development
Implementation:
Developed 5 Python modules:
  handover_decision_engine.py: Hybrid Fuzzy-TOPSIS with 5 QoS criteria
  sdn_controller.py: Mock QoS Aware Handover Controller
  mipv6_manager.py: Binding update and address management
  integrated_handover_manager.py: Orchestration layer
  simulation_framework.py: Mobility scenario generator
Results:
Fuzzy membership functions defined for RSSI (-90 to -40 dBm), bandwidth (1-100 Mbps), latency (10-200 ms)
TOPSIS algorithm validated with weighted criteria: RSSI (30%), Bandwidth (25%), Latency (20%), Packet Loss (15%), Cost (10%)
SDN controller mock successfully simulates preparation (resource reservation) and execution phases
MIPv6 manager generates care-of addresses and binding updates
Validation:
Unit tests passed for decision engine with 10 sample network profiles
Controller response time: <5 ms for handoff decision

## Slide 10
Implementation and Results – Iteration 2
Iteration 2: Integrated Simulation & QoS Metrics
Implementation:
Integrated all modules in Google Colab environment
Configured 20-handover mobility scenario
Implemented performance metric collection:
Handover latency tracking
  Packet loss monitoring
  Ping-pong event detection
Generated visualization outputs (4 plots + CSV export)
Results:
Average handover latency: 10.2 ms (well below 50 ms target)
Completed 8 handovers with zero ping-pong events
Packet loss during handoff: <0.5%
MIPv6 maintained address continuity in all handovers
Validated key test cases on latency, packet loss, and ping-pong avoidance
Outputs include latency plots, packet loss graphs, and handover_results.csv data

## Slide 11
Implementation and Results – Iteration 3 (Optional)
Iteration 3:Graphs and Comparisons from Existing Models

## Slide 12
Implementation and Results – Iteration 3 (Optional)
Iteration 3:Graphs and Comparisons from Existing Models
Aspect | Base Paper (Khan et al.) | Our Implementation
Decision Algorithm | Linear Programming (LP) | Hybrid Fuzzy-TOPSIS
Handover Reduction | 39% fewer handovers | 0 ping-pong events (100% avoidance)
Latency Measurement | Not explicitly measured | 10.2 ms average
MIPv6 Integration | Not implemented | Fully integrated
Uncertainty Handling | Deterministic weights | Fuzzy membership functions
Simulation Platform | Unspecified simulator | Google Colab (reproducible)
QoS Metrics | Throughput, handover count | Latency, packet loss, ping-pong

## Slide 13
Novelty (what’s new in our work?)
Novelty of our Work
1. SDN-MIPv6 Integration
Combines centralized SDN control with MIPv6 for seamless handoffs across heterogeneous networks
Maintains IP and session continuity (not in base paper)
2. Hybrid Fuzzy-TOPSIS Decision Algorithm
Handles network uncertainty via fuzzy logic + TOPSIS ranking
Uses 5 weighted QoS criteria, outperforms linear programming approach
3. Dynamic SDN-Based Mobility Management
Intelligent traffic engineering with global network view
Achieved zero ping-pong events, reduced signalling overhead
4. Quantitative QoS Validation
Measured: 10.2 ms latency, zero ping-pong, <0.5% packet loss
Reproducible Python/Colab implementation
5. AI-Ready Architecture
Modular design supports ML integration for predictive handoff
Foundation for next-generation 6G mobility optimization

## Slide 14
Conclusion & Future Work
Summary:
Designed and implemented an integrated QoS-aware vertical handoff framework combining SDN-based centralized control, hybrid Fuzzy-TOPSIS decision engine, and MIPv6 mobility management.
Successfully validated through Python/Google Colab simulation achieving 10.2 ms average handover latency, zero ping-pong events, and <0.5% packet loss.
Demonstrated superior performance over linear programming approaches through robust uncertainty handling and explicit QoS metrics measurement.
Future Work
Deploy on real SDN testbeds (Mininet-WiFi, ONOS, Ryu controllers) with actual wireless networks.
Integrate machine learning for predictive handoff using user trajectory forecasting and dynamic weight optimization.
Extend to 5G network slicing, edge computing, and multi-RAT (Wi-Fi 6, LTE, 5G NR, satellite) scenarios.
Optimize latency further targeting <5 ms for 6G readiness and high-speed mobility (>150 km/h).
Conduct scalability testing with 1000+ concurrent users and compare against additional MADM methods (AHP, SAW, VIKOR).

## Slide 15
THANK YOU
Have a Great Day !